## Slide 1
⚙ Stepper Motor Open-Loop Simulation
Step Loss Demonstration Using Pulley-Weight Mechanism
Technical Guide for Laboratory Education
Python + Tkinter | Real-Time Interactive Simulation
Author: NANDHAKUMAR J
PPR: 200
Radius: 20mm
Step Angle: 1.8°
T_avail: 1.0 Nm

## Slide 2
Table of Contents
1. Introduction to Stepper Motors
2. Open-Loop vs Closed-Loop Control
3. Step Loss Phenomenon
4. Pulley-Weight Load Mechanism
5. Physics & Mathematical Model
6. Simulation Architecture
7. User Interface Overview
8. Step-by-Step Operating Guide
9. Experimental Observations
10. Key Formulas Summary
11. Applications & Industry Use
12. Conclusion & Learning Outcomes
Learning Objectives
● Understand stepper motor open-loop behavior
● Observe step loss under varying loads
● Analyze torque vs load characteristics
● Interpret displacement error data
● Identify motor stall conditions
Prerequisites
▸ Basic knowledge of electric motors
▸ Understanding of torque and force
▸ Familiarity with Python (optional)
▸ Basic control systems concepts

## Slide 3
1. Introduction to Stepper Motors
Fundamentals of discrete-step rotary actuation
What is a Stepper Motor?
A stepper motor is a brushless DC electric motor that divides a full rotation into a number of equal steps. It can be commanded to move and hold at any one of these steps without any position feedback sensor (open-loop control). Each step corresponds to a fixed angular displacement (e.g., 1.8°).
Key Specifications
● Step Angle: 1.8° (200 steps per revolution)
● Pulses Per Revolution (PPR): 200
● Holding Torque: 1.0 Nm (simulation parameter)
● Control: Open-loop — no encoder feedback
● Drive Method: Pulse/direction digital signals
● Type Used: NEMA-23 hybrid stepper
Types of Stepper Motors
1. Variable Reluctance (VR)
→ Simple construction, low torque
2. Permanent Magnet (PM)
→ Better torque, lower resolution
3. Hybrid Stepper (Used in this simulation)
→ Combines VR and PM advantages
→ High torque + high resolution
→ Most common in CNC, 3D printers
How Stepping Works
Each electrical pulse sent to the motor driver causes the rotor to advance by exactly one step angle (1.8° for 200-step motor). Full rotation = 200 pulses × 1.8° = 360° The pulse frequency determines the rotation speed (RPM). RPM = (Frequency × 60) / PPR

## Slide 4
2. Open-Loop vs Closed-Loop Control
Understanding why step loss occurs in open-loop systems
Open-Loop Control
(Used in this simulation)
✗ No position feedback sensor
✗ Controller assumes all steps executed
✗ Cannot detect or correct step loss
✗ Fails under excessive load
✓ Simple wiring — pulse & direction only
✓ Lower cost — no encoder needed
✓ Works well within torque limits
⚠ KEY PROBLEM: If the load torque exceeds the motor's holding torque, steps are lost — the controller doesn't know, leading to positioning errors!
Closed-Loop Control
(For comparison — not simulated)
✓ Has position feedback (encoder)
✓ Controller verifies step execution
✓ Detects and corrects step loss
✓ Reliable under variable loads
✗ Higher cost — requires encoder
✗ More complex wiring & firmware
✗ Needs PID tuning
✓ ADVANTAGE: Closed-loop systems can compensate for step loss by detecting position errors and issuing corrective pulses, ensuring accurate positioning.

## Slide 5
3. Step Loss Phenomenon
What happens when load exceeds motor capability
Definition
Step loss occurs when the motor's rotor fails to follow the commanded step sequence. The motor receives electrical pulses, but the rotor cannot mechanically advance due to insufficient torque to overcome the load. The controller is unaware of the loss (open-loop), resulting in a growing error between expected and actual position.
Step Loss Conditions
▶ T_required > T_available → STEP LOSS
▶ T_required >> T_available → MOTOR STALL
▶ T_required ≤ T_available → NORMAL (no loss)
▶ Higher RPM → lower available torque → more loss
▶ Heavier load → higher required torque → more loss
Consequences of Step Loss
✗ Positioning error accumulates
✗ No self-correction mechanism
✗ Workpiece damage in CNC
✗ Print failure in 3D printing
✗ Complete stall if severe
Step Loss vs Motor Stall
Step Loss (Partial): Motor still rotates but misses some steps. actual_steps = commanded × (T_avail / T_req) Motor Stall (Complete): Motor completely stops rotating. Occurs when T_req >> T_avail (ratio < 10%) Motor vibrates but cannot advance.

## Slide 6
4. Pulley-Weight Load Mechanism
Converting rotary motion to linear displacement with load
Mechanism Components
1. Stepper Motor — generates step-wise rotation
2. Shaft — transmits rotation to pulley
3. Pulley (r = 20mm) — converts rotation to linear motion
4. String — wraps around pulley, connects to weight
5. Hanging Weight (0–15 kg) — creates resistive load
6. Linear Scale — measures displacement
7. Pointer — indicates position on scale
Direction Convention
▲ LIFT (Forward): Motor rotates Counter-Clockwise (CCW)
Weight moves UP, pointer moves right
▼ LOWER (Reverse): Motor rotates Clockwise (CW)
Weight moves DOWN, pointer moves left
How Load is Applied
The hanging weight creates a gravitational force: F = m × g This force acts through the pulley radius to create torque: T_required = F × r = m × g × r When lifting, the motor must overcome this gravitational torque. If T_required > T_available, step loss occurs. Example: 5 kg weight with 20mm pulley T_req = 5 × 9.81 × 0.02 = 0.981 Nm
Critical Load Threshold
The maximum load before step loss: m_max = T_available / (g × r) m_max = 1.0 / (9.81 × 0.02) m_max ≈ 5.1 kg ▶ Below 5.1 kg: No step loss (green zone) ▶ Above 5.1 kg: Step loss begins (orange zone) ▶ Above ~50 kg: Motor stall (red zone)

## Slide 7
5. Physics & Mathematical Model
Core equations governing the simulation
① Linear Displacement
D = (steps / PPR) × 2πr
Where: steps = commanded pulses, PPR = 200, r = 0.02 m
② Torque Required
T_required = m × g × r
Where: m = load mass (kg), g = 9.81 m/s², r = 0.02 m
③ Step Loss Condition
IF T_req ≤ T_avail: actual_steps = commanded_steps (no loss) IF T_req > T_avail: actual_steps = commanded × (T_avail / T_req) steps_missed = commanded - actual_steps
Worked Examples
Example 1: No Step Loss (3 kg load, 1000 steps) ━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━ T_req = 3 × 9.81 × 0.02 = 0.589 Nm T_req (0.589) ≤ T_avail (1.0) → No loss! actual_steps = 1000 displacement = (1000/200) × 2π × 0.02 × 1000 = 628.32 mm Example 2: Step Loss (8 kg load, 1000 steps) ━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━━ T_req = 8 × 9.81 × 0.02 = 1.570 Nm T_req (1.570) > T_avail (1.0) → STEP LOSS! ratio = 1.0 / 1.570 = 0.637 actual_steps = 1000 × 0.637 = 637 steps missed = 1000 - 637 = 363 steps expected disp = 628.32 mm actual disp = 400.25 mm error = 228.07 mm

## Slide 8
6. Simulation Architecture
Software design and animation engine
Technology Stack
▸ Language: Python 3.x
▸ GUI: Tkinter (built-in)
▸ Animation: Canvas + after()
▸ Physics: Custom engine
▸ No external dependencies
Core Modules
▸ PhysicsEngine — torque/step calculations
▸ StepperSimApp — main application class
▸ Canvas Renderer — 2D mechanical drawing
▸ Animation Loop — 60 FPS via after(16ms)
▸ Data Logger — timestamped event log
Animation Pipeline
1. Calculate dt (time delta)
2. Advance step counter by stepRate × dt
3. Compute actual steps (with loss)
4. Update pulley angle
5. Redraw canvas
6. Update data panel
7. Schedule next frame (16ms)
Three-Panel Layout Architecture
LEFT: Control Panel
Motor Start/Stop Direction toggle Speed slider (0–300 RPM) Load slider (0–15 kg) Step input field Reset button
CENTER: Simulation
Canvas-based 2D animation Motor block + shaft Rotating pulley with spokes String + hanging weight Linear ruler scale Green/Red position markers
RIGHT: Data Display
Expected displacement (mm) Actual displacement (mm) Error & missed steps Load vs Error graph Motor status & progress Timestamped data log

## Slide 9
7. User Interface Overview
Visual elements and their functions
Control Panel Elements
▶ Start Button — begins step execution
■ Stop Button — halts motor immediately
▲ LIFT (CCW) — motor lifts weight up
▼ LOWER (CW) — motor lowers weight
◈ Speed Slider (0–300 RPM)
◈ Load Slider (0–15 kg)
⌨ Step Input — commanded steps
↺ Reset — returns to initial state
Simulation Canvas
⬛ Motor Block — NEMA-23 representation
LED indicator: Green=running, Red=stall
⊕ Rotating Pulley — 4-spoke with direction dot
│ String — connects pulley to weight
▬ Hanging Weight — shows mass label (kg)
━ Linear Ruler — ±250mm scale range
▲ GREEN marker — expected position (EXP)
▲ RED marker — actual position (ACT)
Δ Error bracket — shows displacement error
⚠ Warning overlay — Step Loss / Motor Stall
↺/↻ Rotation direction indicator
Data Display
DISPLACEMENT Section:
Expected (mm) — green
Actual (mm) — red
Error (mm) — orange
STEP ANALYSIS:
Commanded steps
Achieved steps
Missed steps — red
MOTOR STATUS:
Current RPM
Direction (CCW/CW)
Progress %
GRAPH: Load vs Step Error
DATA LOG: Event history

## Slide 10
8. Step-by-Step Operating Guide
How to run the simulation experiment
Step 1
Launch the Application
Run: python stepper_simulation.py The app opens maximized with dark engineering theme.
Step 2
Set Parameters
• Adjust Speed slider (recommended: 60–120 RPM) • Set Load slider (start at 0 kg) • Enter commanded steps (e.g., 1000)
Step 3
Choose Direction
• Click LIFT (CCW) to lift weight upward • Click LOWER (CW) to lower weight down
Step 4
Run Simulation
• Click ▶ Start to begin • Watch pulley rotate & weight move • Observe green/red markers on ruler
Step 5
Observe Step Loss
• Increase load above 5.1 kg • Click Start again — markers diverge! • Check data panel for error values
Step 6
Analyze Results
• Compare Expected vs Actual displacement • Note: Steps Missed count • Review Load vs Error graph

## Slide 11
9. Experimental Observations
Expected results from the simulation experiments
Load (kg)
T_req (Nm)
T_avail (Nm)
Status
Steps Cmd
Steps Actual
Missed
Error (mm)
0.0
0.000
1.000
✓ Normal
1000
1000
0
0.000
2.0
0.392
1.000
✓ Normal
1000
1000
0
0.000
5.0
0.981
1.000
✓ Normal
1000
1000
0
0.000
5.1
1.001
1.000
⚠ Step Loss
1000
999
1
0.628
7.0
1.373
1.000
⚠ Step Loss
1000
728
272
170.8
10.0
1.962
1.000
⚠ Step Loss
1000
509
491
308.3
12.0
2.354
1.000
⚠ Step Loss
1000
424
576
361.7
15.0
2.943
1.000
⚠ Step Loss
1000
339
661
415.2
Key Observations
● Step loss begins exactly at 5.1 kg (when T_req exceeds T_avail of 1.0 Nm)
● At 10 kg load, approximately 49% of steps are lost — nearly half the intended displacement
● The relationship between load and step loss is non-linear (inversely proportional)
● Error accumulates — at 15 kg, the actual displacement is only 34% of expected

## Slide 12
10. Key Formulas Summary
Complete mathematical reference
Linear Displacement
D = (steps / PPR) × 2πr
Converts step count to linear distance in meters. PPR = 200 pulses/rev, r = 0.02 m (pulley radius)
Torque Required
T_req = m × g × r
Gravitational torque from hanging load. m = mass (kg), g = 9.81 m/s², r = 0.02 m
Step Loss Ratio
ratio = T_avail / T_req
Fraction of commanded steps actually executed. ratio ≥ 1: no loss, ratio < 1: step loss occurs
Actual Steps
actual = commanded × min(1, ratio)
Number of steps the motor can physically execute. Steps missed = commanded − actual
Max Safe Load
m_max = T_avail / (g × r)
Maximum load before step loss begins. For this sim: 1.0/(9.81×0.02) = 5.097 kg
Step Rate
f = (RPM / 60) × PPR
Steps per second at given RPM. At 60 RPM: (60/60)*200 = 200 steps/sec

## Slide 13
11. Applications & Industry Use
Where stepper motors and step loss awareness matter
CNC Machines
Stepper motors drive X/Y/Z axes. Step loss causes dimensional errors in machined parts. Load monitoring is critical.
3D Printers
FDM printers use steppers for extrusion and positioning. Step loss creates layer shifts and print failures.
Robotics
Robotic arms and mobile robots use steppers for joint control. Step loss leads to positioning errors and collisions.
Medical Devices
Infusion pumps and diagnostic equipment require precise dosing. Step loss can have critical safety implications.
Textile Machines
Sewing and embroidery machines use steppers for pattern accuracy. Step loss ruins the production output.
Astronomy
Telescope mounts use steppers for star tracking. Even 1 missed step causes tracking errors over long exposures.

## Slide 14
12. Conclusion & Learning Outcomes
What You Learned
✓ Open-loop stepper motors assume perfect step execution
✓ Step loss occurs when load torque exceeds motor torque
✓ The error is proportional to the overload ratio
✓ No feedback = no correction (cumulative error)
✓ Motor stall is the extreme case of step loss
✓ Proper motor sizing prevents step loss
✓ Closed-loop systems solve step loss problems
Key Takeaway
Always size your stepper motor to provide sufficient torque margin (typically 50-100% safety factor) above the maximum expected load. If position accuracy is critical, consider closed-loop stepper systems with encoder feedback.
Possible Extensions
1. Add microstepping (1/2, 1/4, 1/8, 1/16 step modes)
2. Implement speed-torque curve (torque drops at higher RPM)
3. Add closed-loop feedback simulation for comparison
4. Simulate motor heating and thermal derating
5. Add acceleration/deceleration ramp profiles
6. Multiple axis simulation (X, Y, Z)
7. Export data to CSV for lab reports
8. Connect to real hardware via serial/Bluetooth

## Slide 15
Thank You!
Stepper Motor Open-Loop Simulation
Questions & Discussion
Author: NANDHAKUMAR J
Built with Python + Tkinter | No external dependencies | Open Source